## Slide 1: PERMEABILITY ESTIMATION THROUGH INTEGRATION OF VELOCITY, RESISTIVITY, AND PORE GEOMETRY
Ralf J. Weger and Gregor P. Eberli

## Slide 2: Why should you care?
The relationships between velocity, resistivity, and porosity provide insight about pore geometry, connectivity, and permeability.
Direct permeability measurements (core plugs) are expensive, slow, spatially limited, and often unavailable.
Acoustic/Resistivity (EM) data can provide a continuous, indirect permeability estimate.
Utilizing existing (routinely acquired) logging data (sonic, resistivity) for permeability estimation is cheaper and faster than coring and core analysis.
Ralf J. Weger, 2024

## Slide 3
Acoustic Velocity, Electrical Resistivity, and Permeability

## Slide 4: Quantification of Pore Structure
  Produce quantitative description of pore systems characteristics.
  Explain variation in elastic parameters using DIA parameters.

## Slide 5: Linking Pore Structure and Frame Flexibility
Marine and Petroleum Geology 155 (2023) 106359

## Slide 6: Key Points
Ralf J. Weger, 2024
Simple Pores = High Velocity/Permeability:
  Rocks with large pores and simple pore geometries have high acoustic velocity and generally high permeability.
Oomoldic/moldic pores (dissolved grains) are simple (e.g. high velocity) but isolated, causing low permeability.
Low-perm moldic rocks are rare in calcite (greenhouse times) but more common in aragonite (icehouse times).
Isolated moldic pores cause high resistivity (low conductivity), identifying low permeability.

## Slide 7: Velocity-Porosity colored by Geometry
0
5
10
15
20
25
30
35
Porosity (%)
3000
4000
5000
6000
7000
Velocity (m/s)
Cretaceous
Miocene
Mississippien
Neogene
Permiam
0
5
10
15
20
25
30
35
Porosity (%)
3000
4000
5000
6000
7000
Velocity (m/s)
Cretaceous
Miocene
Mississippien
Neogene
Permiam
1
1.2
1.4
1.6
1.8
2
2.2
2.4
2.6
2.8
Log10(PoA)
1.4
1.6
1.8
2
2.2
2.4
2.6
2.8
Log10(DomSize)
from Weger et.al., 2024

## Slide 8: Contact Cements in Carbonates
Marine Microbial Cement
Cretaceous offshore Brazil
Holocene Beach Rock, Shroud Cay
Meniscus Cement
Pleistocene Shoal Ocean Cay
Meteoric Meniscus Cement
Generally producing
high-velocity
high-K rocks
In carbonates, contact cementation occurs as:
  meniscus cements derived from meteoric waters (Harris, 1978; Longman, 1980) or
  micritic bridging cements in the marine realm (Hillgärtner et al., 2001).

## Slide 9: Precipitation of Contact Cements at Sea and in the Lab
In vitro fused 60 days
Fused grains at Joulter Cays
In vitro fused 30 days
400 µm
500 µm
500 µm
Synergetic effects of microbes and EPS as well as calcifying filaments trigger the precipitation of micrite cement in less than 30 days.
Diaz et al., 2022.

## Slide 10: Observe Contact Cements Precipitation in the Lab
Ralf J. Weger, 2024

## Slide 11
Precipitation at grain-to-grain contacts resulted in an increase in velocity comparable with model predictions from the EBT
Intrapore growth at grain surfaces and within pore spaces creates a softer, more complex framework resulting in smaller-than-expected velocity increases despite substantial porosity reduction
Selective removal of non-load-bearing particles during dissolution experiments
simplifies the pore network, increases porosity, but causes only modest velocity
changes
Weger et al., (in review)

## Slide 12: How does Geometry relate to Permeability
0
5
10
15
20
25
30
35
Porosity (%)
-2
-1
0
1
2
3
4
Permeability (log10(mD))
Cretaceous
Miocene
Mississippien
Neogene
Permiam
-2
-1
0
1
2
3
4
Permeability (log10(mD))
0
5
10
15
20
25
30
35
Porosity (%)
Cretaceous
Miocene
Mississippien
Neogene
Permiam
1
1.2
1.4
1.6
1.8
2
2.2
2.4
2.6
2.8
Log10(PoA)
1.4
1.6
1.8
2
2.2
2.4
2.6
2.8
Log10(DomSize)
from Weger et.al., 2024

## Slide 13: EBT on log scale
From well log sonic data to permeability estimates using Extended Biot Theory

## Slide 14:  and Permeability Indicator from Seismic Data
Eberli, G. P., Massaferro, J.‐L., Weger, R. J., Sun, Y. F., Baechle, G. T., and Bracco Gartner, G.,
Permeability from Seismic in Carbonate Reservoirs, Part I: Dream or Reality?, in Proceedings AAPG Annual Convention 2006.
Bracco Gartner, G. L., Weger, R. J., Nasser, M., Leguijt, J., van der Kolk, K., Hillgaertner, H., Asyee, W., Eberli, G. P., Sun Y. F., and Wagner, P.,
Permeability from Seismic in Carbonate Reservoirs, Part II: The Field Example, in Proceedings AAPG Annual Convention 2006.
gk
Permeability
Indicator
Porosity
Applying EBT to reservoir scale QI on high resolution Seismic data can be used to determine volumes and producibility.
Notes: This was used to characterize a reservoir, but the same tools allow for characterization of a potential CO2 container.
BUT, this is based on one-time, static snapshot of a reflection seismic cube

## Slide 15: The Challenge:
Distinguish Simple Pore Space Geometries (stiff rocks) that have connected pore networks from those with unconnected pore networks
Both of these rocks have:
low PoA and high DOM size.
high velocities for their given porosity
low γk
vs.
Almost all rocks fitting this description have excellent flow properties,
But,
some oomoldic/moldic rocks have little to no Permeability

## Slide 16
Aragonite vs calcite seas
Potential for
moldic rocks
Potential for
moldic rocks
Potential for
moldic rocks

## Slide 17: Same high velocity but different permeability
lower
PoA
higher
PoA
lower
k
higher
k
-1
0
1
2
3
4
log
10
(K)
Moldic (separate vug) porosity: pore filling cements form stiff frame
High porosity
High velocity
Low K
Interparticular porosity:
Cements on grain contacts
form rigid frame
High porosity
High velocity
High K

## Slide 18: Same velocity but different permeability
Moldic (separate vug) porosity: pore filling cements form stiff frame
High porosity
High velocity
Low K
Interparticular porosity:
Cements on grain contacts
form rigid frame
High porosity
High velocity
High K

## Slide 19: Linking Resistivity to Pore geometry
  Produce quantitative description of pore systems characteristics in the context of electrical resistivity.
  Explain variation in Archie’s cementation factor using DIA parameters and number of pores.

## Slide 20: Pore Structure and Electrical Resistivity
Verwer et al., 2010

## Slide 21: Cementation Factor, Pores & Pore Number
Phi
NPORES
NTHROATS
DOMsize
PoA
34%
14
39
1500 mm
3 mm-1
Phi
NPORES
NTHROATS
DOMsize
PoA
34%
52
154
730 mm
5.8 mm-1
More pores = less tortuous and higher surface conductivity

## Slide 22: Velocity & Resistivity
1
0
2
0
3
0
4
0
Porosity (%)
3
4
5
6
Velocity (km/s)
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
0.45
Formation Factor (-)
Porosity (fraction)
101
102
103
104
2
3
4
5
6
7
gk
3
4
5
6
7
8
9
Extended Biot Theory gk
m=1
m=2
m=3
m=4
m=5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
4.5
5.0
m (-)
Archie’s Cementation Factor m
(or gk & m)

## Slide 23: Permeability and Electrical Resistivity
Weger et al., 2024
Moldic (separate vug) porosity: pore filling cements form stiff frame with little to no pore connections
High porosity
High velocity
Low conductivity
Low K
Interparticular porosity:
Cements on grain contacts
alllow for large number of pores and pore connections
High porosity
High velocity
High conductivity
High K

## Slide 24: Key Points
Ralf J. Weger, 2024
Simple Pores = High Velocity/Permeability:
  Rocks with large pores and simple pore geometries have high acoustic velocity and generally high permeability.
Oomoldic/moldic pores (dissolved grains) are simple (e.g. high velocity) but isolated, causing low permeability.
Low-perm moldic rocks are rare in calcite (greenhouse times) but more common in aragonite (icehouse times).
Isolated moldic pores cause high resistivity (low conductivity), identifying low permeability.

## Slide 25: Questions?

## Slide 26: Resistivity Measurements
AutoLab 1000
NER
m = −log(Ro/Rw) / log(φ)
F=f-m where,
F=Ro/Rw
Ro= Rt/Sw-n
f = porosity
F = formation resistivity factor
Ro = resistivity of fully saturated rock
Rt = resistivity of partially saturated rock
Rw = resistivity of pore fluid
Sw = brine saturation
n = saturation exponent
m = cementation factor

## Slide 27: Comparison of Data Sets
 | Mean Phi | Median Phi | Mean FF | Median FF | Mean m | Median m | # of Sample
Reefal | 30.2 | 27.2 | 74 | 55 | 3.21 | 3.11 | 66
Hamelin Pool | 28.5 | 29.6 | 44 | 27 | 2.65 | 2.63 | 64
Stromatolites | 19.2 | 19.5 | 349 | 57 | 2.45 | 2.28 | 72
Tufa | 18.8 | 18.5 | 216 | 121 | 2.87 | 2.83 | 12
MISS Dolo. | 15.6 | 15.1 | 233 | 76 | 2.27 | 2.32 | 14
Travertine | 9.9 | 8.2 | 6597 | 3773 | 3.38 | 3.25 | 77
LLL | 6.3 | 6.8 | 392 | 371 | 2.06 | 2.14 | 13
VM | 6.6 | 5.3 | 651 | 342 | 1.94 | 1.93 | 166
ET | 7.7 | 8.0 | 580 | 355 | 2.20 | 2.25 | 58
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
0.45
Formation Factor (-)
Porosity (fraction)
101
102
103
104
m=1
m=2
m=3
m=4
m=5
Reefal Limest.
Stromatolites
Hamelin Pool
Travertine
MISS Dolo.
Tufa
VM
LLL
Klaas Verwer, Albertus Ditya, Ergin Karaca, Jan Norbisrath, Giovanna della Porta
+ 224 VM samples
= 542 samples
Reefal
Hamelin Pool
Strom.
Tufa
MISS
Dolomites
Travertine
LLL
VM
ET
1
2
3
4
5
m (-)
Kruskal-Wallis test
318 samples
 | Mean Phi | Median Phi | Mean FF | Median FF | Mean m | Median m | # of Sample
Reefa | 30.2 | 27.2 | 74 | 55 | 3.21 | 3.11 | 66
Hamelin Pool | 28.5 | 29.6 | 44 | 27 | 2.65 | 2.63 | 64
Stromatolites | 19.2 | 19.5 | 349 | 57 | 2.45 | 2.28 | 72
Tufa | 18.8 | 18.5 | 216 | 121 | 2.87 | 2.83 | 12
MISS Dolo. | 15.6 | 15.1 | 233 | 76 | 2.27 | 2.32 | 14
Travertine | 9.9 | 8.2 | 6597 | 3773 | 3.38 | 3.25 | 77
LLL | 6.3 | 6.8 | 392 | 371 | 2.06 | 2.14 | 13
ET

## Slide 28: Comparing Cementation Factors
Reefal Limestones
(Ditia 2011)
Carbonates
(Verwer 2011)
Stromatolites
Travertine
and Tufa
Crystalline Dolomite
(crystal sizes 30-300mm)
VM Mudstone
m = 2.11 - 5.29
m = 1.7 - 4.14
m = 1.9 - 5.8
m = 1.75 - 3.01
m = 1.13 - 2.96
Mudstones and Crystalline Dolomite have a narrow range and very low m
Crystalline Dolomite have a narrow range and still low m
Stromatolites have a narrow range and higher m
Travertine and Reefal Limestones have a wide range and often very high m
m = 2.1 – 3.8

## Slide 29: Stiff rock frames. What is it, and what creates it?
High velocity at a given porosity is possible if pore compressibility is low
Stiff frames occur in rocks with vugs or molds, but also in rocks with interparticle and intercrystalline porosity.
From the latter, stiff frames can be produced by contact cementation (Dvorkin and Nur, 1996)

## Slide 30: Cementation Theory
Dvorkin & Nur, 1996
Grains interact through cement that strengthen the most compliant part of the pore space — the grain contacts.
cementation scheme 1, first and foremost, increases rock stiffness due to increased grain-to-grain contact strength
The main practical conclusion is that high porosity — high velocity
indicates well cemented grain contacts and
a mechanically strong and stable potential reservoir rock.