## Slide 1: Microbially Induced Permeability Reduction: Example of Project SEALOR for South Florida Flood Management
Alexander Suma, Robert Smith, and Ralf J. Weger

## Slide 3
One night of rain, August 8th, 2025
Bottom-Up Flooding, King Tide 2024

## Slide 4: Why should you care?
SEALOR represents a unique intersection of carbonate sedimentology, energy transition, and applied subsurface engineering.
The approach provides:
Flood & Infrastructure Protection: Enabling long-lasting, low-toxicity reinforcement of porous carbonates, directly relevant to coastal urban resilience.
Carbon Sequestration: Permanent mineralization of CO₂, aligned with global decarbonization goals.
New Pathways for Carbonate Engineering: Insights into pore-filling, strength enhancement, and permeability control in carbonate reservoirs, directly translating to subsurface storage, enhanced recovery, and wellbore stabilization.
Industrial Synergies: Oil and gas companies exploring Carbon Capture, Utilization & Storage (CCUS) and reservoir integrity can adapt SEALOR ’s methodology in carbonate formations globally.

## Slide 5
Sea Walls
Saltwater Intrusion

## Slide 6
Neal et al., 2008
Caglar Usdun
Florida Geological Survey News and Research - September 2019

## Slide 7
Florida’s to layer composition
~3ft of dirt
~30ft of Miami Oolite
Miami Oolite
Average 37% cavity
Up to 60% cavity space in matrix
Miami Limestone

## Slide 8
Joulters Cay – experiment comparison
Fused grains at Joulter Cays
In vitro Fused grains (60 days)
Notes: Joulters Cay

## Slide 9
This process can improve shear strength to stabilize slopes in rivers, canal banks and natural hills.
It can reduce settlement on foundations by filling voids with calcite particles.
It can also increase the stiffness of soil to prevent liquefaction in seismic prone areas.

## Slide 10: The Technology - Sealor
1. Microbe Production Facility
2. Transport All Ingredients to Site
3. Final Mixing On-Site
4. Inject Sealor into the Ground
5. Sealor Creates an Underground Impermeable Barrier with High Strength Properties
PATENTED TECHNOLOGY

## Slide 11
Potential Carbon Sequestation Impact
44% of Newly Formed Limestone is Sequestered CO2 Locked in the Underground for Eternity
CaCO3

## Slide 12
Phase 1 Proof of Concept
Chips ✔️
1.5x1.5cm
Autoclaved
Cylindrical hole in center
Observed hole filling in
20% weight addition
10 days MICP
Completed
Cubes Set 1 ✔️
2x2x1cm
Autoclaved
Test different MICP cocktails
Observe forming CaCO3
30 days MICP ✔️
Measure weight addition
2x30 days MICP to go
Completed
Control
Cubes Set 2
2x2x1cm
Non-Autoclaved
Test different MICP cocktails
Observe forming CaCO3
90 days MICP
Measure porosity change
Ongoing
MICP here used as Microbially Induced Carbonate precipitation

## Slide 13
Initial Lab Results
06/24/25 07/03/25 07/27/25
This is the same rock!
9 days
24 days
+25% Weight in 30 days

## Slide 14
Dry Rock
CO2 Induced
Carbonate Precipitation
1 week
CO2 & Microbially Induced
Carbonate Precipitation
1 week + 1 week
CO2 & Microbially Induced
Carbonate Precipitation
1 week + 2 week
Testing of CO2 & Microbially Induced Carbonate Precipitation

## Slide 15
Phase 1 Proof of Concept
Plugs
1x2 inch
Autoclaved
Petrophysics impermeability
(University of Miami)
90 days MICP
Ongoing
Flat Rock
30x30x4cm
Autoclaved
Observe forming CaCO3
Scaling up
Weight & Volume measurement
90 days MICP
Ongoing
Volumatic rock
20x20x25cm
Non-Autoclaved
Mimic field conditions
Observe forming CaCO3
Weight & Volume measurement
90 days MICP
Planned
TRL 3
TRL 4
TRL 5

## Slide 16
Test Setup
3 injection points
10ft deep, expected 10-15ft radius spread
Summer 2026
3rd Party validations
Next step: pilots
Phase 2: Field Test (TRL 6)
TEST LOCATION
60x60FT FENCED
WORK PACE: 60x60 FT FENCED
INJECTION 1: 15 FT DIAMATER CIRCLE
3x10 FT TRENCH
INJECTION 2: 3x (12.5x7.5 FT) OVALS
3x10 FT TRENCH
INJECTION 3: 5x (10x5 FT) OVALS

## Slide 17
Ralf J. Weger, 2024
0.1
0.2
0.3
0.4
1
2
3
4

## Slide 18
Testing Precipitation on Plug samples with both DI Water and Seawater

## Slide 19: Key Points
Ralf J. Weger, 2024
“SEALOR” Technology uses Microbially Induced Carbonate Precipitation to create a subsurface barrier that strengthens the subsurface to reduce permeability and mitigate seawater infiltration and flooding.
  It aims to enhance coastal resilience by protecting infrastructure
  It acts as a carbon-negative solution, permanently sequestering CO₂ underground.
“SEALOR” can be used for both Infrastructure Protection & Carbon Sequestration.
This ongoing NSF-SBR uses over over 150 lab tests to confirm the method's effectiveness:
  a) calcium carbonate crystal formation,
  b) pore-space reduction, and
  c) significant consolidation of sediment samples
Quantification and large-scale field testing is still ongoing …

## Slide 20: Questions?